## Slide 1
CMOS Logic Gate Design
Ref: Designing Combinational Logic Gates in CMOS -CHAPTER 6, Jan Rabey

## Slide 2: Static CMOS Circuit
At every point in time (except during the switching transients) each gate output is
connected to either
V
DD
or
V
ss
via a low-resistive path
The outputs of the gates assume at all times the value of the Boolean function,
implemented by the circuit (ignoring the transient effects during switching periods)
This is in contrast to the
dynamic
circuit class, which relies on temporary
storage of signal values on the capacitance of high impedance circuit nodes

## Slide 3: Static Complementary CMOS
VDD
F(In1,In2,…InN)
In1
In2
InN
In1
In2
InN
PUN
PDN
PMOS only
NMOS only
PUN and PDN are dual logic networks
…
…
Notes: One and only one of the networks (PUN or PDN) is conducting in steady state

## Slide 4: NMOS Transistors in Series/Parallel Connection
    Transistors can be thought as a switch controlled by its gate signal
    NMOS switch closes when switch control input is high

## Slide 5: PMOS Transistors in Series/Parallel Connection

## Slide 6: Threshold Drops
VDD
VDD  0
PDN
0  VDD
CL
CL
PUN
VDD
0  VDD - VTn
CL
VDD
VDD
VDD  |VTp|
CL
S
D
S
D
VGS
S
S
D
D
VGS
Notes: Why PMOS in PUN and NMOS in PDN … threshold drop
NMOS transistors produce strong zeros; PMOS transistors generate strong ones

## Slide 7: Complementary CMOS Logic Style

## Slide 8: Example Gate: NAND

## Slide 9: Example Gate: NOR

## Slide 10: Complex CMOS Gate
OUT = D + A • (B + C)
D
A
B
C
D
A
B
C
Notes: Shown synthesis of pull up from pull down structure

## Slide 11: Constructing a Complex Gate

## Slide 12: Cell Design
Standard Cells
  General purpose logic
  Can be synthesized
  Same height, varying width
Datapath Cells
  For regular, structured designs (arithmetic)
  Includes some wiring in the cell
  Fixed height and width

## Slide 13: Standard Cell Layout Methodology – 1980s
signals
Routing
channel
VDD
GND
Notes: Contacts and wells not shown.
What does this implement??

## Slide 14: Standard Cells
In
Out
V
DD
GND
In
Out
V
DD
GND
With silicided diffusion
With same diffusion

## Slide 15: Standard Cells
A
Out
V
DD
GND
B
2-input NAND gate

## Slide 16: Stick Diagrams
Contains no dimensions
Represents relative positions of transistors
In
Out
V
DD
GND
Inverter
A
Out
V
DD
GND
B
NAND2

## Slide 17: Stick Diagrams
C
A
B
X = C • (A + B)
B
A
C
i
j
j
VDD
X
X
i
GND
A
B
C
PUN
PDN
A
B
C
Logic Graph
Notes: Systematic approach to derive order of input signal wires so gate can be laid out to minimize area
Note PUN and PDN are duals (parallel <-> series)
Vertices are nodes (signals) of circuit, VDD, X, GND and edges are transitions

## Slide 18: Two Versions of C • (A + B)
X
C
A
B
A
B
C
X
VDD
GND
VDD
GND
Notes: Line of diffusion layout – abutting source-drain connections
Note crossover eliminated by A B C ordering

## Slide 19: Multi-Fingered Transistors
One finger
Two fingers (folded)
Less diffusion capacitance

## Slide 20: CMOS Properties
Full rail-to-rail swing; high noise margins
Logic levels not dependent upon the relative device sizes; ratioless
Always a path to Vdd or Gnd in steady state; low output impedance
Extremely high input resistance; nearly zero steady-state input current
No direct path steady state between power and ground; no static power dissipation
Propagation delay function of load capacitance and resistance of transistors

## Slide 21: Switched Delay Model
A
Req
A
Rp
A
Rp
A
Rn
CL
A
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint
B
Rp
A
Rp
A
Rn
B
Rn
CL
Cint
NAND2
INV
NOR2
Capacitance on the internal node – due to the source drain of the two MOSFETs in series
Notes: Note capacitance on the internal node – due to the source drain of the two fets in series

## Slide 22: Input Pattern Effects on Delay
Delay is dependent on the pattern of inputs
  Both inputs go low
    Delay is 0.69 rp/2 CL
  One input goes low
    Delay is 0.69 rp CL
  Both inputs go high
    Delay is 0.69 2Rn CL
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint

## Slide 23: Delay Dependence on Input Patterns
A=B=10
A=1, B=10
A=1 0, B=1
time [ps]
Voltage [V]
Input Data Pattern | Delay (psec)
A=B=01 | 67
A=1, B=01 | 64
A= 01, B=1 | 61
A=B=10 | 45
A=1, B=10 | 80
A= 10, B=1 | 81
NMOS = 0.5m/0.25 m
PMOS = 0.75m/0.25 m
CL = 100 fF
Notes: Gate sizing should result in approximately equal worst case rise and fall times.
Reason for difference in the last two delays is due to internal node capacitance of the pulldown stack. When A transitions, the pullup only has to charge CL; when A=1 and B transitions pullup have to charge up both CL and Cint.
For high to low transitions (first three cases) delay depends on state of internal node. Worst case happens when internal node is charged up to VDD – VTn.
Conclusions: Estimates of delay can be fairly complex – have to consider internal node capacitances and the data patterns.

## Slide 24: Transistor Sizing
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint
B
Rp
A
Rp
A
Rn
B
Rn
CL
Cint
2
2
2
2
1
1
4
4
Notes: Assumes Rp = Rn

## Slide 25: Transistor Sizing
Reference Inverter
CMOS NOR gate implementation

## Slide 26: Transistor Sizing
It is possible to extend this same design technique to create multiple input NOR gates

## Slide 27: Transistor Sizing a Complex CMOS Gate
OUT = D + A • (B + C)
D
A
B
C
D
A
B
C
1
2
2
2
4
4
8
8
Notes: For class lecture.
Red sizing assuming Rp = Rn
Follow short path first; note PMOS for C and B 4 rather than 3 – average in pull-up chain of three – (4+4+2)/3 = 3
Also note structure of pull-up and pull-down to minimize diffusion cap at output (e.g., single PMOS drain connected to output)
Green for symmetric response and for performance (where Rn = 3 Rp)
Sizing rules of thumb
PMOS = 3 * NMOS
1 in series = 1
2 in series = 2
3 in series = 3
etc.

## Slide 28: Fan-In Considerations
D
C
B
A
D
C
B
A
CL
C3
C2
C1
tpHL = 0.69 Reqn(C1+2C2+3C3+4CL)
Propagation delay deteriorates rapidly as a function of fan-in
Notes: While output capacitance makes full swing transition (from VDD to 0), internal nodes only transition from VDD-VTn to GND
C1, C2, C3 on the order of 0.85 fF for W/L of 0.5/0.25 NMOS and 0.375/0.25 PMOS
CL of 3.2 fF with no output load (all diffusion capacitance – intrinsic capacitance of the gate itself).
To give a 80.3 psec tpHL (simulated as 86 psec)

## Slide 29: tp as a Function of Fan-In
tpLH
tp (psec)
fan-in
Gates with a fan-in greater than 4 should be avoided.
tpHL
quadratic
linear
tp
tpLH increases linearly due to the linearly increasing value of the diffusion capacitance
tpHL increase quadratically due to the simultaneous increase in pull-down resistance and internal capacitance
tpLH
Notes: Fixed fan-out (NMOS 0.5 micrcon, PMOS 1.5 micron)
tpLH increases linearly due to the linearly increasing value of the diffusion capacitance
tpHL increase quadratically due to the simultaneous increase in pull-down resistance and internal capacitance

## Slide 30: tp as a Function of Fan-Out
tpNOR2
tp (psec)
eff. fan-out
tpNAND2
tpINV

## Slide 31: Fast Complex Gates: Design Technique 1
1.Transistor sizing
2. Progressive sizing
InN
CL
C3
C2
C1
In1
In2
In3
M1
M2
M3
MN
M1 > M2 > M3 > … > MN
FET closest to the output is the smallest
M1 have to carry the discharge current from M2, M3, … MN and CL so make it the largest
MN only has to discharge the current from MN (no internal capacitances)
Notes: M1 have to carry the discharge current from M2, M3, … MN and CL so make it the largest
MN only has to discharge the current from MN (no internal capacitances)

## Slide 32: Fast Complex Gates: Design Technique 2
Transistor ordering
C2
C1
In1
In2
In3
M1
M2
M3
CL
C2
C1
In3
In2
In1
M1
M2
M3
CL
critical path
critical path
charged
1
01
charged
charged
1
Delay determined by time to discharge CL, C1 and C2
Delay determined by time to discharge CL
1
1
01
charged
discharged
discharged
Place latest arriving signal (critical path) closest to the output
Notes: For lecture.
Critical input is latest arriving signal
Place latest arriving signal (critical path) closest to the output

## Slide 33: Fast Complex Gates: Design Technique 3
Alternative logic structures
F = ABCDEFGH
Notes: Reduced fan-in -> deeper logic depth
Reduction in fan-in offsets, by far, the extra delay incurred by the NOR gate (second configuration).
Only simulation will tell which of the last two configurations is faster, lower power

## Slide 34: Fast Complex Gates: Design Technique 4
Isolating fan-in from fan-out using buffer insertion
CL
CL
Notes: Reduce CL on large fan-in gates, especially for large CL, and size the inverters progressively to handle the CL more effectively

## Slide 35: Ratioed Logic

## Slide 36: Ratioed Logic

## Slide 37: Active Loads

## Slide 38: Dynamic Logic

## Slide 39: Dynamic CMOS
In static circuits at every point in time (except when switching) the output is connected to either GND or VDD via a low resistance path.
  fan-in of n requires 2n (n N-type + n P-type) devices
Dynamic circuits rely on the temporary storage of signal values on the capacitance of high impedance nodes
  requires on n + 2 (n+1 N-type + 1 P-type) transistors

## Slide 40: Dynamic Gate
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out
CL
Out
Clk
Clk
A
B
C
Mp
Me
Two phase operation
Precharge (Clk = 0)
Evaluate (Clk = 1)
on
off
1
off
on
((AB)+C)
Notes: For lecture
Evaluate transistor, Me, eliminates static power consumption

## Slide 41: Conditions on Output
Once the output of a dynamic gate is discharged, it cannot be charged again until the next precharge operation
Inputs to the gate can make at most one transition during evaluation
Output can be in the high impedance state during and after evaluation (PDN off), state is stored on CL
Notes: This behavior is fundamentally different than the static counterpart that always has a low resistance path between the output and one of the power rails.

## Slide 42: Properties of Dynamic Gates
Logic function is implemented by the PDN only
  number of transistors is N + 2 (versus 2N for static complementary CMOS)
Faster switching speeds
  Due to the reduced number of transistors in the circuit and the single transistor load per fan-in, the load capacitance for the circuit is substantially lower than for static CMOS
  No Isc, so all the current provided by PDN goes into discharging CL
Overall power dissipation usually higher than static CMOS
  no static current path ever exists between VDD and GND (including Psc)
  no glitching
Notes: CL being lower also contributes to power savings

## Slide 43: Properties of Dynamic Gates
PDN starts to work as soon as the input signals exceed VTn, so VIH and VIL equal to VTn
  low noise margin (NML)
Needs a precharge/evaluate clock